|  | Statistical Office of the Republic of Serbia |  |
| --- | --- | --- |
|  |  | ISSN 0353-9555 |
| STATISTICAL RELEASE | ZS10 |
| Number 151 - Year LXVI, 17/06/2016 |  |
| Environmental statistics | SERB151 ZS10 170616 |

Protection against damaging water effects in the Republic of Serbia, 2015

– Preliminary results –

The data represent the preliminary results of the annual survey referring to protection against flood and river control, land drainage, land erosion control and torrent regulation in 2015.

Starting from 1999 the Statistical Office of the Republic of Serbia has not at disposal and may not provide available certain data relative to AP Kosovo and Metohia and therefore these data are not included in the coverage for the Republic of Serbia (total).

Area flooded by surface waters was 36 752 hectares, of which 78.1% referred to utilised agricultural land.

The total area defended from flooding amounted to 1 121 492 hectares, presenting the decrease of 15.5%, compared to 2014. Utilised agricultural land represented 84.8% of the area defended from flooding, showing the decrease of 17.6%, compared to 2014.

System of drainage area decreased by 0.7% relative to 2014, while the length of drainage canals was by 23.5% longer than the referent values in the previous year.

Graph 1. Total and utilised agricultural areas flooded by surface waters in the Republic of Serbia, 2013–2015

*) Estimation.

Graph 2.Total and utilised agricultural areas defended against flood in the Republic of Serbia, 2013–2015

1. Protection against damaging water effects, 2015 by Regions

|  | Republic of Serbia |
| --- | --- |
|  | Total | Beogradski region | Vojvodina | Region Šumadije i Zapadne Srbije | Region Južne I Istočne Srbije |
| Areas and facilities flooded by surface water |
| Total flooded area, ha | 36 752 | 2 295 | - | 26 887 | 7 570 |
| Utilised agricultural area, ha | 28 730 | 918 | - | 21 154 | 6 658 |
| Settlements, number | 239 | - | - | 110 | 129 |
| Buildings, number | 7 414 | - | - | 6 823 | 591 |
| Industrial facilities, number | 117 | - | - | 90 | 27 |
| Other industrial facilities, number | 272 | - | - | 236 | 36 |
| Railway lines, km | 37 | - | - | 34 | 3 |
| Roads, km | 710 | - | - | 595 | 115 |
| Areas and facilities flooded by ground water |
| Total flooded area, ha | 5 399 | - | - | 1 423 | 3 976 |
| Utilised agricultural area, ha | 4 158 | - | - | 1 177 | 2 981 |
| Settlements, number | 58 | - | - | 37 | 21 |
| Buildings, number | 996 | - | - | 861 | 135 |
| Industrial facilities, number | 47 | - | - | 43 | 4 |
| Other industrial facilities, number | 352 | - | - | 352 | - |
| Railway lines, km | 1 | - | - | - | 1 |
| Roads, km | 37 | - | - | 17 | 20 |
| Areas and facilities protected against floods |
| Total area protected against floods, ha | 1 121 492 | 60 319 | 783 340 | 215 046 | 62 787 |
| Utilised agricultural area, ha | 951 896 | 52 029 | 699 300 | 163 148 | 37 419 |
| Settlements, number | 634 | 37 | 175 | 244 | 178 |
| Industrial facilities, number | 1 061 | 11 | 633 | 303 | 114 |
| Other industrial facilities, number | 13 897 | 120 | 1 782 | 8 987 | 3 008 |
| Railway lines, km | 745 | 46 | 333 | 152 | 214 |
| Roads, km | 3 474 | 70 | 1 782 | 781 | 841 |
| Total length of embankment, km | 3 065 | 572 | 1 305 | 741 | 447 |
| Drainage |
| Total area covered by drainage system, ha | 2 378 651 | 348 411 | 1 744 842 | 199 187 | 86 211 |
| Utilised agricultural area covered by drainage system, ha | 1 703 496 | 71 903 | 1 394 552 | 152 892 | 84 149 |
| Drainage canals, km | 7 030 | 1 058 | 5 213 | 448 | 311 |
| Pumping stations, number | 201 | 31 | 127 | 18 | 25 |
| Land erosion |
| Eroded land, km2 | 4 776 | 1 300 | - | 2 753 | 723 |
| Reclaimed land, km2 | 686 | - | - | 530 | 156 |

2. Floods and protection against damaging water effects, 2013–2015

Republic of Serbia

|  | 2013 | 2014 | 2015 |
| --- | --- | --- | --- |
| Areas and facilities flooded by surface water |
| Total flooded area, ha | 22 3991) | 130 837 | 36 752 |
| Utilised agricultural area, ha | 19 4711) | 91 382 | 28 730 |
| Settlements, number | 62 | 1 136 | 239 |
| Industrial facilities, number | 35 | 296 | 117 |
| Railway lines, km | 4 | 52 | 37 |
| Roads, km | 427 | 2 314 | 710 |
| Areas and facilities flooded by ground water |
| Total flooded area, ha | 125 | 15 157 | 5 399 |
| Utilised agricultural area, ha | 115 | 12 867 | 4 158 |
| Settlements, number | 5 | 80 | 58 |
| Industrial facilities, number | 6 | 19 | 47 |
| Railway lines, km | 1 | - | 1 |
| Roads, km | 8 | 28 | 37 |
| Areas and facilities protected against floods |
| Total area protected against floods, ha | 1 248 741 | 1 326 167 | 1 121 492 |
| Utilised agricultural area, ha | 1 088 863 | 1 156 517 | 951 896 |
| Settlements, number | 603 | 833 | 634 |
| Industrial facilities, number | 506 | 666 | 1 061 |
| Railway lines, km | 553 | 631 | 745 |
| Roads, km | 2 304 | 4 118 | 3 474 |
| Total length of embankments, km | 2 884 | 3 242 | 3 065 |
| Drainage |
| Total area covered by drainage system, ha | 2 131 678 | 2 395 519 | 2 378 651 |
| Utilised agricultural area covered by drainage system, ha | 1 705 308 | 1 816 375 | 1 703 496 |
| Drainage canals, km | 5 601 | 5 692 | 7 030 |
| Pumping stations, number | 223 | 3 762 | 201 |
| Land erosion |
| Eroded land, km2 | 6 996 | 9 444 | 4 776 |
| Reclaimed land, km2 | 277 | 811 | 686 |

1) Estimation.

Methodological explanations on protection against damaging water effects can be found on the SORS website: http://webrzs.stat.gov.rs/WebSite/Public/PageView.aspx?pKey=201.

Data series on protection against damaging water effects are available as a part of the SORS publications: http://webrzs.stat.gov.rs/WebSite/Public/PageView.aspx?pKey=200.

Contact: neda.cukavac@stat.gov.rs ; dusanka.dostanic@stat.gov.rs phone: 011/3290242

Printed and published by: Statistical Office of the Republic of Serbia, Belgrade, Мilana Rakica 5 
Telephone: +381 11 2412-922 • Fax: +381 11 2411-260 • www.stat.gov.rs
Responsible: Dr Miladin Kovačević, Director

Circulation: 20 ● Issued annually