|  | Statistical Office of the Republic of Serbia | ISSN 0353-9555 |
| --- | --- | --- |
| STATISTICAL RELEASE | ZS50 |
| Number 156 • Year LXVII, 23/06/2017 |  |
| Environmental statistics | SERB156 ZS50 230617 |

Water use and protection against pollution, 2016

– Preliminary results –

The data represent the preliminary results on abstracted, used, discharged, reused water from industry a in 2016.

In 2016, water abstraction was by 24,1% increased relative to 2015, whereof, in 2016 1.9% more ground and spring water was abstracted and 24.4% more surface water.

1.  Abstracted, used, discharged, reused water from industry and water losses from industry,

2014–2016

Republic of Serbia                                                                                                                                                               mill. m3

|  | 2014 | 2015 | 2016 |
| --- | --- | --- | --- |
| Abstracted water1) | 2 693 | 3 324 | 4 127 |
| Water use 1) | 2 693 | 3 324 | 4 127 |
| Discharged water1) | 2 660 | 3 290 | 4 094 |
| Treated water | 85 | 99 | 103 |

1) Water used for hydropower plants is excluded.

Of the total 4 127 mill. m3 of abstracted waters, 99.6% are from self-supply (surface water – 98.9%, ground water 0.7%) and 0.4% is from public water supply.

2. Water abstraction from industries, by type of supply system, 2016

Republic of Serbia

|  | Total, mill. m3 | Percentage of abstracted water from public water supply | Percentage of abstracted water from self-supply |
| --- | --- | --- | --- |
|  |  |  | Ground water | Surface water |
| Abstracted water1)2 | 4 127 | 0,4 | 0,7 | 98,9 |
| Mining and quarrying | 9 | 4,0 | 21,7 | 74,3 |
| Manufacturing | 119 | 11,4 | 21,6 | 67,0 |
| Electricity, gas , steam and air conditioning supply | 3 997 | 0,1 | 0,1 | 99,8 |

1) Water used for hydropower plants, which is not included in this table, in 2016 amounted 185 865 mill. m3.

2) Water use includes division Waste collection, treatment and disposal activities; materials recovery.

Out of the total used water in industries, 96.9% refers to water used in section Electricity, gas, steam and air conditioning supply, 2.9% to water used in Manufacturing, while 0.2% relates to water used in Mining and quarrying.

3. Water use in industry, by type of use, 2016

Republic of Serbia                                                                                                                                                                mill. m3

| Division (CA) | Total1) | Cooling water for electricity generation | Other cooling water | Water in technological process | Sanitary water | Other industrial use of water |
| --- | --- | --- | --- | --- | --- | --- |
| Water use2) | 4 127 | 3 945 | 57 | 58 | 11 | 55 |
| Mining and quarrying | 9 | - | 0 | 7 | 1 | 1 |
| Manufacturing industry | 119 | 1 | 57 | 45 | 8 | 8 |
| Manufacture of food products and beverages | 23 | - | 3 | 13 | 3 | 5 |
| Manufacture of textiles, wearing apparel and leather and related products | 3 | - | 0 | 2 | 1 | 0 |
| Manufacture of paper and paper products | 3 | - | 0 | 3 | 0 | 0 |
| Manufacture of coke and refined petroleum products, chemicals and chemical products and basic pharmaceutical products and pharmaceutical preparations | 52 | 1 | 39 | 10 | 1 | 1 |
| Manufacture of basic metals | 26 | - | 14 | 12 | 1 | 0 |
| Manufacture of motor vehicles, trailers and semi-trailers and other transport equipment | 1 | - | 0 | 1 | 0 | 0 |
| Other manufacturing industry4) | 10 | - | 1 | 5 | 2 | 2 |
| Electricity, gas, steam and air conditioning supply | 3 997 | 3 944 | 0 | 6 | 2 | 45 |

1) In total water use in industry is included evaporated water used for cooling purposes.

2) Water used for hydropower plants, which are not included in this table, in 2016 amounted 185 865 mill. m3.

3) Water use includes division Waste collection, treatment and disposal activities; materials recovery.

4) Manufacture of tobacco products, Manufacture of wood and of products of wood and cork, except furniture, Printing and reproduction of recorded media,  Manufacture of rubber and plastic products, Manufacture of other non-metallic mineral products, Manufacture of fabricated metal products, except machinery and equipment, Manufacture of computer, electronic and optical products, Manufacture of electrical equipment, Manufacture of machinery and equipment, Manufacture of furniture, Other manufacturing, Repair and installation of machinery and equipment.

Of the total disharged wastewater from industry, 97.3% comes from section Electricity, gas, steam and air conditioning supply, 2.6% from Manufacturing and 0.1% from Mining and quarrying.

4. Discharged water from industry, 2016

Republic of Serbia                                                                                                                                                                                        mill. m3

|  | Total | Discharged water, of which: |
| --- | --- | --- |
|  |  | For cooling | Untreated wastewater |
| Discharged water1)2) | 4 094 | 4 002 | 92 |
| Mining and quarrying | 4 | 0 | 4 |
| Manufacturing industry | 106 | 58 | 48 |
| Electricity, gas, steam and air conditioning supply | 3 983 | 3 944 | 39 |

1) In total discharged water, water used for hydropower plants are not included.

2) Water use includes division Waste collection, treatment and disposal activities; materials recovery.

5. Treated and reused water from industry, 2016

Republic of Serbia                                                                                                                                                                                       mill. m3

|  | Treated discharged water | Reused water |
| --- | --- | --- |
|  | Total | Primary treatment | Secondary treatment | Tertiary treatment |  |
| Treated1) and reused water | 103 | 91 | 9 | 4 | 1 |
| Mining and quarrying | 2 | 1 | 1 | 0 | 0 |
| Manufacturing industry | 45 | 34 | 7 | 4 | 0 |
| Electricity, gas, steam and air conditioning supply | 56 | 56 | 1 | - | 1 |

1) Water use includes division Waste collection, treatment and disposal activities; materials recovery.

Methodological notes

Starting from 1999 the Statistical Office of the Republic of Serbia has not at disposal and may not provide available certain data relative to AP Kosovo and Metohia and therefore these data are not included in the coverage for the Republic of Serbia (total).

Methodological explanations on Water use and protection against pollution can be found on the SORS website: http://webrzs.stat.gov.rs/WebSite/Public/PageView.aspx?pKey=201

Data series on Water use and protection against pollution are available within the  SORS database: http://webrzs.stat.gov.rs/WebSite/public/ReportView.aspx , and as a part of the SORS publications: http://webrzs.stat.gov.rs/WebSite/Public/PageView.aspx?pKey=200.

Contact:ana.vignjevic@stat.gov.rs phone: 0113290242 Information and dissemination unit, phone: 011/2401284 Published and printed by: Statistical Office of the Republic of Serbia, Milana Rakica 5, Belgrade Phone: +381 11 2412922 ● Fax: +381 11 2411260 ● www.stat.gov.rs Responsabile: Dr Miladin Kovačević, Director Circulation: 20 • Issued annually